## Slide 1: Linking water quantity and water quality via aquatic vegetation processes
Ellis Penning, Jasper Dijkstra

## Slide 2: Why vegetation modelling?
Vegetation is important: Ecosystem services
  Wave attenuation
  Erosion prevention
  Habitat for many animals
  Primary production
  Legislation
  Water quality
Transparent tools to answer quantitative questions
  Water management
Notes: Terminology ecologists/modellers

## Slide 3: Goal of this presentation
To give you a flavour of various recent developments in the Deltares software:
  Vegetation and Water quantity: Dynveg, D3D-flow, Xbeach, SWAN
  Vegetation and Water quality: Delwaq, Habitat
To give some examples of recent applications
  Paulina schor (water quantity)
  Veluwemeer (water quality)
To invite you to work with us in the further development of our knowledge on quantifying the effect of macrophytes

## Slide 4: Process based modelling
  Vegetation and Water quantity
Model | Scale | Process
Dynveg | individual plant – patch scale | flow
Delft3D-Flow | meadows in rivers, estuaries, coasts | flow and transport
Xbeach | nearshore meadows | (long) waves
SWAN | nearshore meadows | (short) waves
Development model

## Slide 5: Dynveg
1DV flow interaction between flow and flexible vegetation
  plant drag depends on orientation in flow; dynamic feedback
  k-epsilon turbulence model
  real plant properties (buoyancy, elasticity)
  can be coupled to Delft3D for 2/3D
Notes: Explain colors: status

## Slide 6: Delft3D
Spatial effect of vegetation on flow:
  k-epsilon turbulence model: ‘rigid rods’
  Trachytopes
Notes: Jasper, beide voorbeelden zijn in 1DV!

## Slide 7
Example: Paulinaschor
Stijn Temmerman
University of Antwerp
Formerly at NIOZ/NIOO-CEME

## Slide 8
Example: Paulinaschor
Temmerman S, Bouma TJ, Govers G, Wang, ZB, de Vries MB, Herman, PMJ. 2005. Impact of vegetation on flow routing and sedimentation patterns: Three-dimensional modeling for a tidal marsh. Journal of Geophysical Research-Earth Surface 110 (F4): Art. No. F04019.

## Slide 9: Linking processes – water quantity
Flow velocity
Attenuation
Inundation characteristics
Drought characteristics
Colonization
Development
Mortality
Propagule
dispersal
Vegetation
Flow (regime)
Sedimentation
Erosion
Hydromorphology
Substrate conditions
Burial
Scouring
Hydraulic resistance
Cohesion
Delft3D-Flow

## Slide 10
Example: intertidal flat
Rigid vegetation
Flexible vegetation
T0: Tidal flat MSL+1.4m , random vegetation seeding, 4.5m tide
Temmerman, S., T.J. Bouma, J. Van de Koppel, D. Van der Wal, M.B. De Vries, P.M.J. Herman. 2007. Vegetation causes channel erosion in a tidal landscape. Geology.

## Slide 11
Summarizing: feedback mechanisms between plants and water quantity are important….
And how about plants and water quality?

## Slide 12
Spatial patterns in Lake Veluwemeer, 1994
(Van den Berg & Coops, 1998)
Chara cover
(%)
Light attenuation (m-1)
Inorganic Susp.Sed.
(mg L-1)
Organic Susp. Sed
(mg L-1)
Chlorophyl-a
(ug L-1)
Sedimentation
Speed
(g m-2 d-1)
HCO3-
(mg L-1)
PO4-P
(ug L-1)
NH4-N
(mg L-1)
NO3-N
(mg L-1)

## Slide 13: Why a macrophyte module in Delwaq?
Delwaq before
Need for clear water situations predictions and hindcasting
Society: nuicance – ‘aquatic weeds’ , nutrient pumps => internal eutrophication
Water Framework Directive : macrophytes are good!
On-line community
Would like to model the role of vegetation, especially macrophytes, but also other vegetation, in water quality modelling
Vegetation = terrestrial/aquatic,/woody/flexible
Macrophyte = (semi-)aquatic, (semi-)flexible

## Slide 14: Processes – water quality
Seasonal fluctuations
Clear or turbid state
Higher trophic levels
grazing
Competition
Development
Mortality
Suitable
Habitat
Vegetation
Algae
Nutrient cycling
Light/temperature
Water/soil chemistry
Substrate conditions
Burial/storage
Nutrient pump
Total primary production
Uptake/excretion
Limiting factors
DELWAQ

## Slide 15
emergent
submergent
roots
rhizome
detritus (water)
detritus (sediment)
dissolved nutrients (water)
dissolved nutrients (sediment)
decay
decay
uptake
storage
transport
storage
transport
respiration
transport
respiration
respiration
sedimentation
resuspension
uptake
uptake
water
sediment
(2)
(1)
(9)
(6)
(12)
(3)
(8)
(11)
(10)
(7)
(4)
(5)
storage
DELWAQ: nutrient cycles
grazing
(some) existing DELWAQ modules
New Macrophyte Module
Algae - BLOOM

## Slide 16
Most prominent features
Plants can have roots, rhizomes, submerged and emerged sections
Up to 5 generic plants compete for resources (salt & fresh water)
Vertically structured biomass in water and soil
Competition with algae for light and nutrients (N, P, C)
Uptake from roots or shoots depending on availability and preference
Feedback to D3D-flow 1DV-plants feature (see poster Qinghua Ye)
Basic grazing/harvest function

## Slide 17
Nuphar lutea (source: M.Moeys
Potamogeton perfoliatius
(source: M. Moeys)
Emergent
Submergent
Floating rooted
Floating unrooted
Floating submergent
Stratiotes aloides (source The Virtual Field-Guide )
Phragmites australis
(source Photo © M. Savela )
Lemna sp. (source M.Moeys)
Plant morphologies
Notes: different macrophyte growth forms based on different morphology/functioning
emergent: rooted with most of the leaf above water. not modeled
Submergent: rooted with all system under water. also macroalgae like characeae family
Floating rooted: underwater with leaves floatinf on the surface
floating unrooted: free floatin, small roots in the water
foating submergent: part floating, part submergent , roots in the water

## Slide 18: Vertically structured: lineair / exponential
F = 0.001 | F = 5 | F = 20
Linear or exponential distribution of biomass over the vertical layers
Biomass is vertically distributed
This is input for the sub-modules that require such distribution:
  vertical distribution of light extinction
  => (self)shading and competition with other macrophytes and algae)
  Nutrient uptake per layer (and thereby competition with other prim.prod.)
  Feedback to D-FLOW

## Slide 19: Biomass growth per layer

## Slide 20: resuspension of sediments
Dynamic spatially distributed biomass modelling in lake Veluwemeer, via DELWAQ macrophyte module
Using substrate and exposure as initial HABITAT criteria for growth (Workshop B)
biomass distribution
Notes: Note that the vegetation patch added to the maps on bottom shear stress shows a different shape than the modelled vegetation. This was done because we want to see more explicitly the functioning of the patch. it is a first, and therefore artificial trial. the biomass distribution uses a habitat suitability index procedure but is seasonally dynamic implemented in delwaq. light=> 4% must reach the bottom, temperature follows a sine function through the season, substrate must be sand, exposure to waves makes limited when depth is shallower than 20 cm. in the white area on the left side the lake is too deep. biomass only grows in the shallow areas on the right.

## Slide 21
bed shear stress without macrophytes
bed shear stress with macrophytes
suspended inorganic matter without winddriven currents
with winddriven currents without macrophytes
with winddriven currents and macrophytes
jan feb mar apr may june july aug sept oct nov dec ‘94
jan feb mar apr may june july aug sept oct nov dec ‘94

## Slide 22
bed shear stress
inorganic suspended matter
1-7-’94
No plants
No plants
plants
plants

## Slide 23
Seagrass
Dense seagrass
No vegetation
Rigid vegetation
Light at seabed
Difference in light reaching the bed
Example: link to water quality
Dijkstra JT, van Katwijk MM, (subm) Seagrass meadows reduce flow and sediment transport and improve underwater light climate. Validation and vegetation-scenario runs of a morphodynamic model. Submitted to Estuarine Coastal Shelf Science.

## Slide 24
Thank you

## Slide 25
Thank you